## Slide 1: Radiologie 1
<number>
Notes: While you are stepping through the metal detector, your carry-on items are going through the X-ray system. A conveyor belt carries each item past an X-ray machine. X-rays are like light in that they are electromagnetic waves, but they are more energetic, so they can penetrate many materials. The machine used in airports usually is based on a dual-energy X-ray system. This system has a single X-ray source sending out X-rays, typically in the range of 140 to 160 kilovolt peak (KVP). KVP refers to the amount of penetration an X-ray makes. The higher the KVP, the further the X-ray penetrates.
<number>

## Slide 2: Radiologie 1
<number>
Notes: A common misconception is that the X-ray machine used to check carry-on items will damage film and electronic media. In actuality, all modern carry-on X-ray systems are considered film-safe. This means that the amount of X-ray radiation is not high enough to damage photographic film. Since electronic media can withstand much more radiation than film can, it is also safe from damage. However, the CT scanner and many of the high-energy X-ray systems used to examine checked baggage can damage film (electronic media is still safe), so you should always carry film with you on the plane.
<number>

## Slide 3: Radiologie 1
<number>
Notes: The voltage difference between the cathode and anode is extremely high, so the electrons fly through the tube with a great deal of force. When a speeding electron collides with a tungsten atom, it knocks loose an electron in one of the atom's lower orbitals. An electron in a higher orbital immediately falls to the lower energy level, releasing its extra energy in the form of a photon. It's a big drop, so the photon has a high energy level -- it is an X-ray photon.
<number>

## Slide 4: Radiologie 1
<number>
Notes: The free electron collides with the tungsten atom, knocking an electron out of a lower orbital. A higher orbital electron fills the empty position, releasing its excess energy as a photon.
<number>

## Slide 5: Radiologie 1
<number>
Notes: Vacuum buis in een loden omhulling
<number>

## Slide 6: Radiologie 1
<number>
Notes: Op de kathode (knap) wordt met een laag voltage een wolfraam draadje aan het gloeien gebracht
<number>

## Slide 7: Radiologie 1
<number>
Notes: De kathode krijgt een kapje: de elektronen willen weg van de kathode
<number>

## Slide 8: Radiologie 1
<number>
Notes: De wolfraam anode met draaischijf trekt de elektronen aan
<number>

## Slide 9: Radiologie 1
<number>
Notes: De elektronen botsen door de hoogspanning op de anode. Door de hoek die er in de anode zit ontstaat er een primaire röntgenstraling naar beneden.
De primaire straal wordt begrensd door het diafragma.
<number>

## Slide 10: Radiologie 1
<number>

## Slide 11: Radiologie 1
<number>
Notes: Met lichtvizier, een lampje bootst de primaire straal na, stel je het diafragma in.
<number>

## Slide 12: Radiologie 1
<number>
Notes: The voltage difference between the cathode and anode is extremely high, so the electrons fly through the tube with a great deal of force. When a speeding electron collides with a tungsten atom, it knocks loose an electron in one of the atom's lower orbitals. An electron in a higher orbital immediately falls to the lower energy level, releasing its extra energy in the form of a photon. It's a big drop, so the photon has a high energy level -- it is an X-ray photon.
<number>

## Slide 13: Radiologie 1
<number>
Notes: Are X-Rays Bad For You? X-rays are a wonderful addition to the world of medicine; they let doctors peer inside a patient without any surgery at all. It's much easier and safer to look at a broken bone using X-rays than it is to open a patient up.
But X-rays can also be harmful. In the early days of X-ray science, a lot of doctors would expose patients and themselves to the beams for long periods of time. Eventually, doctors and patients started developing radiation sickness, and the medical community knew something was wrong.
The problem is that X-rays are a form of ionizing radiation. When normal light hits an atom, it can't change the atom in any significant way. But when an X-ray hits an atom, it can knock electrons off the atom to create an ion, an electrically-charged atom. Free electrons then collide with other atoms to create more ions.
An ion's electrical charge can lead to unnatural chemical reactions inside cells. Among other things, the charge can break DNA chains. A cell with a broken strand of DNA will either die or the DNA will develop a mutation. If a lot of cells die, the body can develop various diseases. If the DNA mutates, a cell may become cancerous, and this cancer may spread. If the mutation is in a sperm or an egg cell, it may lead to birth defects. Because of all these risks, doctors use X-rays sparingly today.
Even with these risks, X-ray scanning is still a safer option than surgery. X-ray machines are an invaluable tool in medicine, as well as an asset in security and scientific research. They are truly one of the most useful inventions of all time.
<number>

## Slide 14: Radiologie 1
<number>
Notes: Benoem de onderdelen van het plaatje: bedieningspaneel, de plaats van de röntgenbuis, kastje met lichtvizier en diafragma, tafel met cassette houder, plaats voor trafo om hoogspanning op te wekken.
<number>

## Slide 15: Radiologie 1
<number>
Notes: Ontwikkelautomaat. Vullen in de doka!
<number>

## Slide 16: Radiologie 1
<number>
Notes: Bescherming tegen röntgenstraling. Welke beschermen tegen de primaire straal? Waar komt de strooistraling vandaan?
<number>

## Slide 17: Radiologie 1
<number>
Notes: Praktijkmanier om hd foto’s te maken
<number>

## Slide 18: Radiologie 1
<number>
Vragen die belangrijk zijn om te beantwoorden:
Waar ontstaat de primaire bundel?
Waar ontstaan strooistralen?
Waarom wordt een rontgenfoto in twee stappen gemaakt?
Waarom moet je even wachten voordat de
eigenlijke foto gemaakt wordt?
Notes: Antwoorden: 1. aan de (draai) anode 2. aan het dier (het object) 3. Kathode moet gaan gloeien, Anode moet gaan draaien.
<number>